## Slide 1: Arm CCA – IOMMU & Trusted Devices
Suzuki K Poulose <suzuki.poulose@arm.com>
20th September
LPC 2024 – CC MC

## Slide 2: Agenda
Arm CCA v1.0 Architecture – Quick Recap
Arm CCA v1.1 – Features
Arm CCA – SMMU and TDISP

## Slide 3: Arm CCA v1.0 - Recap
EL3 Monitor
Linux / KVM
RMM
RSI
Realm A
RMI
Realm B
RSI
VMM
IMPDEF
Root World
VM
Normal World
Realm World
RHI
EL2
EL1
EL0
EL3
RMI – Realm Management Interface
RSI – Realm Service Interface
RHI – Realm Host Interface

## Slide 4: Arm CCA – v1.1
Extension to Arm CCA v1.0 (v1.0-Rel0)
  Compatible with CCA-v1.0 -> [0] https://developer.arm.com/documentation/den0137/latest/
  CCA v1.0 Support patches on List for Linux / VMMs and at: https://gitlab.arm.com/linux-arm/linux-cca
Public version of the spec available here, also linked from [0]
  https://developer.arm.com/-/cdn-downloads/permalink/PDF/Architectures/DEN0137_1.1-alp8_rmm-arch_external.pdf
v1.1: Planes - Multiple privileged levels in Realm VM
  Derek Miller’s Talk on Arm CCA Inter plane communication interface Proposals
v1.1: Device Assignment (DA) - Allow trusted device access to/from Realm Memory
v1.1: Memory Encryption Contexts (MEC)
  Per Realm memory encryption key
v1.1: Firmware Update & Activation
  Update and activate the RMM

## Slide 5: Arm CCA v1.1 – {Secure} Device Assignment
EL3 Monitor
Linux / KVM
RMM (TSM)
RSI++
Realm A
RMI (+DA)
RSI
VMM
IMPDEF
Root World
VM
Normal World
Realm World
RHI (+ DA)
EL2
EL1
EL0
EL3
P0
P1
P2
TEE-Dev
TDISP + IDE

## Slide 6: Arm CCA v1.1 – Device Assignment
RMM takes the role of TSM
  PCI and Platform attested devices
RMM - Device communication via Host - RMI_*DEV_COMMUNICATE
  RMM could ask the host to cache the data (e.g., certificates, interface reports, measurements)
  RMM keeps the digests of the host cached data (for Realm to verify the host provided data)
Establishes S-SPDM session at setup of Physical Device + IDE Keys
  Fetches Certificate chain (Platform devices are attested by RMM Platform Attestation)
    Host caches the certificates, RMM keeps the Digests
Realm initiates the transition, RMM assisted
  Interface report, measurements etc are fetched RMM and cached by host, with digests in RMM

## Slide 7: SMMU with TDISP
The T-bit determines the SMMU SEC_SID value
SEC_SID determines which SMMU interface the transaction is associated with, and therefore the PAS in which the SMMU Stream Table and SMMU translation tables (stage 1 + stage 2) must be placed
T-bit | SEC_SID | SMMU interface | SMMU tables PAS
0 | 0b00 (NS) | NS | NS
1 | 0b10 (Realm) | Realm | Realm
Software impacts for stage 2
  The hypervisor must manage a separate set of tables (Stream Table + S2TT) in NS PAS
  The S2TT must at least contain mappings for MSI targets
T=0 -> SMMU in NS world, Hypervisor
  Stag1 SMMU => Hypervisor emulated
T=1 -> SMMU Driver in RMM, share CPU page tables for Stage2
  Stage1 SMMU => RMM emulated !

## Slide 8: Realm IPA Space
Realm
RMM
Protected IPA space
Unprotected IPA space
Stage 2 translation tables
Hypervisor
MMIO
MMIO
Realm
PA space
MMIO
IPA Space is split, with private and shared halves
Guest sees a single {I}PA space and “treats” the top bit as a “SHARED=1”
All MMIO are emulated by Host “today” with Arm CCA v1.0, i.e., Unprotected MMIO
With CCA v1.1, some of these could be emulated in the Realm world (e.g., SMMU) more on it later (placed in the Protected IPA space)
Guest can check if a given “MMIO” is protected or shared.

## Slide 9: SMMU with “shared” mode and Stage 1 SMMU
Hardware
Realm
RMM
Protected IPA space
Unprotected IPA space
Stage 2 translation tables
(Realm + NS PAS mappings)
Hypervisor
Non-Secure SMMU
TDI, state != RUN
Stage 2 translation tables
(NS PAS mappings only)
vSMMU emulation
Stage 1 translation tables
Unprotected vSMMU
T=0 (DMA, MSI)
When in state != RUN, device operates identically to a non-TDISP device
Guest interacts with Unprotected vSMMU instance
Realm SMMU

## Slide 10: SMMU with “Trusted” mode and Stage 1 SMMU
Hardware
Realm
RMM
Unprotected IPA space
Hypervisor
Non-Secure SMMU
TDI, state == RUN
Stage 2 translation tables
(NS PAS mappings only)
T=0 (MSI)
When device state transitions to RUN, guest must use stage 1 translation tables in Protected IPA space
Thereafter, guest interacts with the Protected vSMMU instance
Protected IPA space
Stage 2 translation tables
(Realm + NS PAS mappings)
Stage 1 translation tables
vSMMU emulation
Protected vSMMU
T=1 (DMA)
Realm SMMU

## Slide 11: Solutions ? RMM vSMMU shadowing
vSMMU emulation
Hardware
Realm
RMM
Protected IPA space
Unprotected IPA space
Stage 2 translation tables
(Realm + NS PAS mappings)
Hypervisor
Non-Secure SMMU
TDI, state != RUN
Stage 2 translation tables
(NS PAS mappings only)
T=0 (DMA, MSI)
In principle, a single guest-facing vSMMU instance could be multiplexed onto two instances, depending on the device state
When device state != RUN, RMM communicates guest’s stage 1 updates and vSMMU commands to hypervisor, via REC exits (new - RMM spec changes required)
Stage 1 translation tables
vSMMU emulation
Protected vSMMU
Realm SMMU
Shadow stage 1 translation tables (NS mappings only)
However, this violates the Realm’s security model: accesses to Protected IPA space are now exposed to / emulated by the Host

## Slide 12: Solutions ? RMM vSMMU shadowing
Hardware
Realm
RMM
Unprotected IPA space
Hypervisor
Non-Secure SMMU
TDI, state == RUN
Stage 2 translation tables
(NS ITS mappings only)
T=0 (MSI)
When device state transitions to RUN, guest continues to use the Protected vSMMU instance, and RMM directs vSMMU commands to the Realm SMMU hardware
Protected IPA space
Stage 2 translation tables
(Realm + NS PAS mappings)
Stage 1 translation tables
vSMMU emulation
Protected vSMMU
T=1 (DMA)
Host must still shadow (at least) the ITS mappings in the NS stage 2 translation tables
Realm SMMU

## Slide 13: Solution? Guest view of Realm and NS vSMMU instances
NS vSMMU in Protected IPA space
Firmware table describes a “container”, within which both instances are mapped
Access to Protected IPA space can be exposed to / emulated by the Host
The Guest driver configures both SMMU instances when in shared mode. Only the “Realm vSMMU” in protected mode.
NS vSMMU in Unprotected IPA space
Firmware table describes the Realm instance
  Mapping to the NS instance is via convention
Access to Protected IPA space remains within Realm TCB
Protected IPA space
Unprotected IPA space
Realm vSMMU
NS vSMMU
Protected IPA space
Unprotected IPA space
Realm vSMMU
NS vSMMU
IPA |= MSB

## Slide 14: Arm CCA – DA flow

## Slide 15: Arm CCA – DA Flow – Step by step
Realm A
RMM
Host
Device
1. Create PDEV object
Establish S-SPDM connection
Provides Certificates to the Host for Caching
Stores Digests in RMM
Programs the IDE Key if applicable
pdev
[digests]
2. Create Realm
vdev (Realm A)
3. Create VDEV object
4. Create Dev mappings
5.2 Request Dev info (RSI)
Get device Interface Report and Measurements
Provides the data for caching at host
Store Digests in RMM
vdev
[digests] (Realm A)
5.3 Request Dev info (RHI)
PDev. Certs
vdev Data
5.4 Request Digests (RSI)
5.5 Verify Certificates, Reports and measurements with Digests
Dev. Creds
[digests]
6. Verify Device mappings
Dev Map Stage2
5.1 Lock the Device (RSI)
TDISP: LOCK
7. Accept the device
TDISP: RUN
Realm Boots up and discovers the device capable of TDISP. Decides to verify
8a. Abort the device
8b. Destroy the vdev
TDI State